# Text boxes

Raysun WEP-30 (A)/(B)

Wireless Digital Monitor Spy Earpiece

- Wireless Bluetooth V2.1 + EDR supports the communication at a distance of 10~15 meters. Wearing the (A) (B) type of stealth earpiece, users can auto answer the incoming calls in private.

- Top quality earpiece with adjustable volume control, and the built-in highly sensitive microphone allows outside callers to automaticlly initiate the bluetooth receiver to intercept communications of its surrounding.

- Select “ Manual answer” or “ Auto answer”.

- Operate with the cellular phone in support of :1. Redial 2. Voice Dialing 3. Music Playback 4. Recording During Communication.

- Receiver can be used as an independent wireless monitor device after being detached with collar ring.

－

18mm

12mm

The content is subject to change without prior notice.

( B )

安全防衛及戰術裝備 – 08B

By adopting “Fleming’s Right Hand Rule” and wireless “Bluetooth V2.1 + DER” on its design, the receiver, being connected with cellular phone and operated via magnetization of stealth wireless earpiece, has gained tremendous improvement in communication safety and power-efficiency.  It is a cutting -edge communication product in modern days, with no RF emission harmful to human body.

＋

When placed in a specific place, users can select "Auto Answer" from the Bluetooth collar receiver to start with a remote telephone link function and initiate a real-time monitoring for outside caller.

WEP-30(B)

Battery Insertion Diagram：

Size Comparison：

＋

WEP-30(A)

( Specification:

| Parts | Invisible Spy Earpiece |
| --- | --- |
| Model | 30A | 30B |
| Transmission | Magnetic |
| Highest output by 3Khz | 110dB |
| Dimension | Diameter: 8mm Length: 12mm | Diameter: 10mm Length: 18mm |
| Weight | Approx. 0.8g | Approx. 0.9g |
| Frequency range | 300 Hz ~ 5 KHz |
| S/N ratio | 50dB to 2 KHz |
| Battery type | SR416W (1.55V) | 10D6 (1.4V) |
| Battery life (Standby mode ) | 6 hours / 72 hours | 40 hours / 144 hours |
| Noise filter | No | Yes |
| Parts | Bluetooth Collar Receiver |
| Bluetooth version | V2.1+ EDR |
| Dimension | Diameter: 1.5 Length:14.5 (cm) |
| Weight | Approx. 35g |
| Battery type | Li-ion Rechargeable |
| Receiver Size | 35mm x 54mm x 13mm |
| Battery life | Standby up to 30 hours / Communicate up to 50 minutes |

( Standard package includes:

(1) Invisible Spy Earpiece 30A or 30B

(2) Bluetooth Spy Pen

(3) Earpiece battery x 6

Users can auto answer the incoming calls by wearing GSM receiver under overcoat and placing ear piece into ear。

( A )

( A )

Micro size, can be fully inserted into ear canel.

( B )

Detachable Bluetooth Receiver design, can be used as an independent monitor device

Mini size, with camouflage coloring.