# Text boxes

Raysun PV-RC1 & RCM

Socket-type Spycam & DIY module

Special surveillance Devices -10

PV-RCM

PV-RC1

- Small size, DIY to become various features (such as: toys, picture frames, brush holders, hand-carried package…and so on) for covert A/V recording.

- High resolution camera with motion detect function, Video: 1280x960/photo: 2560x1920.

- High battery capacity, standby time: 10 hrs.; continuously recording time: approx. 6 hrs.

- Lens flexible flat cable is around 5 cm length for easily flexible installation.

- An ideal type of camouflage record/photo camcorder for secret surveillance task.

- Come with general socket and jack cover plate which can be flexibly exchanged to coupling with main unit by magnetic way easily.

- Simply paste it on a suitable place or in any camouflage box by double-side tape.

- Activated by two modes:

(1). Motion detection mode: for A/V recording only. Standby time: 10 hours.

(2). PIR mode: optionally A/V recording or snapshot (photo). Standby time: up to 10 days above.

Micro camera

Main board

Battery

PV-RC1

PV-RCM (DIY)

( Specifications:

| Model | PV-RC1 | PV-RCM |
| --- | --- | --- |
| Memory | Micro SD HC card |
| Time/date display | Y/M/D/H/M/S |
| Focus range | 15cm~ ∞ |
| Min. illumination | <3Lux |
| Field of view | 65° |
| Activation mode | Motion/PIR detection | Motion detection |
| Detection distance | Max. to 4M, depend on environmental illumination |
| Record mode | Continuously/detected recording(5 minutes/time) |
| Photo mode | PIR detected photo(5 pictures/time) | -- |
| Continuously recording time | 6 hrs above |
| Standby time | Motion detection: 10 hrs above |
|  | PIR detection: 240 hrs above | -- |
| Recording resolution | 1280x960 |
| Frame per second | 29 fps above |
| Photo resolution | 2560x1920 |
| Connection port | USB 2.0 |
| Dimension | Around 116x66x8.9 mm (exclude cover) | As above diagram |
| Weight | Around 65g(exclude cover) | Around 15g(exclude battery) |

Camouflage stick on the wall for auto recording

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.

P.13