# Text boxes

Raysun

3G / 3.5G A/V Transmitter

Security Defense & Tactical Devices – 13-1

- Easy-to-operate.  Connect to PC and press one button to initiate the operation of the device.

- 3.5G high speed transmission provides upload speed up to 5.76 Mbps and 7.2 Mbps download speed.

- After installation of Windows XP / Vista / 7 on PC, you can directly receive the AV signal from 3G/3.5G transmitter for real-time communication/monitoring, and even issue a command through PC.

- Being linked to Google Map, Integrated GPS system allows you trace the physical location easily from the PC.

- Work with all kinds of cam, DV and hidden cam.

- Built-in HCSD slot can support the memory up to 32G in capacity for real-time A/V & GPS signal.

- Compact (135x80x25mm), lightweight (only 240g),   energy-saving allows 3 consecutive hours in use.

Application(2): work with 2.5mm/4-Pin Spy cam.

Application(1): work with general DV / CCD

A / V

Various types of hidden cam

HRL-7/9

3G/3.5G

DVR for monitoring

3G/3.5G

( Specification：

| Processor | TMS320DM355 DaVinci™ |
| --- | --- |
| RAM memory | 1GB DDR2 SDRAM |
| NAND FLASH memory | 1GB NAND FLASH |
| Memory card | Support up to 32 GB SDHC card |
| Micro- USB | For charging use |
| Mini-USB | For AV-input |
| GPS system | Fast positioning to catch up to maximum of 20 satellite channels. DGPS(WAAS, EGNOS, MSAS, RTCM):1-5 m Speed : Without aid: 0.1 M /sec Time : 0.1 ms。(the correspondent of GPS time) |
| 3G HSDPA module | Multi-mode: HSUPA/HSDPA/UMTS/EDGE/GPRS/GSM. HSUPA upload speed: 5.76 Mb ps HSDPA download speed: 7.2 Mbps Transmitting speed of CDMA (UMTS): 384 kbps EDGE download speed: 2 37 Kbps EDGE upload speed: 118Kbps |
| Video processing | High-efficient TVP5146 video decoder with MPEG4 encoding on DM355 。 |
| Audio | Real-time A/V-in/out, also support standard earphones. |
| Audio processor | Adopt ForteMedia FM11 speech processor to provide fluent audio signal. |
| Indicator | Built-in LED illuminator and buzzer for alert |
| Powder supply | Lithium polymer battery, 3200mAH / 3.7V |
| Run time | up to 3.5 hours. |
| Current consumption | Max. :400m A @12VDC , Average: 300m A @ 12VDC Stand-by: 1m A @ 12VDC |
| Size | 135 x 80 x 25 mm |
| Net weight | 240g |

A/V-out to TV for monitoring

( Standard package：

(1). Main unit

(2). 3G antenna

(3). 3200mah Li polymer battery *1

(4). Transformer for Micro USB

(used as a charger)

(5). AV-in cable

(6). Leather pouch

(7). Operation manual/ DVD

( Option：

(1). Raysun HRL-7/9 Multifunctional camcorder／telecom headset.

(2). Raysun hidden camera series

(3). Reinforced vehicle 3G antenna

(4). 3200mah Lithium polymer battery

(5). Vehicle GPS high-gain antenna.

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.