# Text boxes

Raysun FS-EQ/FS-D

Stretchable Video-scope

Special surveillance Devices-17-2

Visible/invisible auxiliary LED light

FS-D

FS-EQ

3 Stretch nodes

Built-in LED lights, and also can work with optionally additional visible / invisible (IR) illuminators to enhance light level.

4 Stretch nodes

Bendable tube

Optionally work on viewing/recording/ wireless transmission applications

- Waterproof, high resolution CCD camera with built-in LED for day/night inspection.

- Stretchable shaft for adjustable working length, light weight, easy operation. General Li-on battery available.

- The bendable semi-rigid tube can be adjusted to get the required viewing angle of the front-end camera with water/oil proof.

- Can additionally add an optional visible / invisible (IR) illuminators to enhance light level.

- Multiple operation modes as following descriptions.

Application (1). FS-EQ/D＋DVR-1 (viewing/recording)

Application (2). FS-EQ/D＋

Wireless transmitter

(transmission)

Application (3). FS-EQ/D＋DVR-2＋Wireless transmitter

(viewing/recording/ transmission)

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.

Choose to work with

JR-1208Pwireless receiver

P.26

or

Monitor

WRD-3 wrist-wear wireless A/V receiver/recorder

( Specifications:

| Model | FS-EQ | FS-D |
| --- | --- | --- |
| Day/night mini color CCD camera | Image sensor | 1∕4” color CCD |
|  | Min. illumination | 1 Lux |
|  | Outer dia. | Φ20×75mm |
|  | Electronic shutter | 1/60～1/120000 |
|  | Pixels | NTSC:768(H)×496(V) |
|  | Power | 123A Lithium Battery *2 |
|  | Video resolution | 520TV Lines |
|  | Battery running time | Around. 240 minutes |
| Shrink length | Semi-rigid tube: 100cm | around 100 cm (Semi-rigid tube: 35cm) |
| Extension length | Around. 175 cm | Around. 211 cm |
| Stretch nodes | 3 | 4 |
| Weight | Around 835g (exclude battery) | Around 585g (exclude battery) |

Co-works with wireless transmitter and WRD-3 wrist-wear wireless A/V receiver/recorder to easily & conveniently operation.

( Options:

- Head-wear monitor

- DVR-1 digital recorder

- DVR-2 digital recorder＋wireless transmitter

- WRD-3 wrist-wear wireless A/V receiver/recorder

- Additional IR LED light

- Additional LED light

本型錄內容說明、規格如有調整修訂，不另通知。