# Text boxes

Raysun FS-EVD-III Plus

IR Video-scope Inspection Device

Special surveillance Devices -18-3

- FS-EVD-III Plus integrates an innovative ultra wide FOV (158∘) miniature IR sensible camera with IR invisible light for wider viewing, better low light condition usage than FS-EVD-III.

- 4-way articulations, over 120∘for each direction. The front-end cam is immersible to water.

- Color/B&W modes auto change at Day/night, clearly viewing/recording image even under lightless environment within around 2M.

- Scaled polyurethane rubber covered tube for well protection & length/depth measurement indication.

- It’s ideal for industry, drainage system, aircraft, national defense, law enforcement, scientific research, …etc applications.

- IR invisible auxiliary light

- 158∘ultra wide FOV IR sensible camera

- Photography/Record/Transmission

- The insertion tube and front-end cam is both immersible to water.

( Remote monitoring

( Image performance

RX

TX

RX

158° ultra wide FOV

Color/B&W modes auto change while low light condition

(1). Transmit A/V signal to WRD-3 wrist-wear wireless A/V receiver/recorder

( Specification:

| Model | FS-EVD-III Plus |
| --- | --- |
| Video resolution | 400TV LINE |
| Image sensor | 1/4 Color CMOS cam |
| Min. illumination | 0.1 Lux / F1.2, effective pixels: 640x480 |
| Electronic shutter | 1/60~1/10000 |
| Lens(FOV) | 2.8mm(F1.2)／158° |
| Auxiliary light | IR960nm LED*6 |
| Tube outer dia. | 8mm |
| Articulations | Up/down/left/right, 360∘full directional |
| Tube operation length | Around 180cm above |
| Wireless transmission | 1200MHZ/6 CH |
| Output power | 200mW(0.2W) |
| Transmission range | Around 100M |
| Battery running time | Around 70 minutes |
| Power | 3.6V/1800mA |
| Dimension(exclude sticking out part) | Around 300 x110x90mm |
| Weight | Around 870g |
| Record resolution | 720 x480@18fps 640x480@30fps |
| Memory | SD HC card |
| Date/time record | Y/M/D/H/M/S |
| Low power indication | yes |

( Features

(2). Transmit A/V signal to JR1208P wireless A/V receiver and output it to the connected monitor

( Standard package:

- FS-EVD-III plus main body

- Aluminum hard suitcase

Isolate between camera & IR light

The length measurement can indicate the inserting length/depth easily.

P.29

>240°

Full direction control

( Option:

- JR1208P wireless A/V receiver

- WRD-3 wrist-wear wireless A/V receiver/recorder

Articulations control

360∘4-way turning

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.