# Text boxes

Raysun NVS-14

Multi-functional Night Vision Monocular

Optics & Night Vision Devices - 25

P.36

Add a 20X room lens lens

Helmet-wear

Head-wear

5. Co-work with camcorder

Quickly mount to weapon

( Specifications:

| Model | NVS 14-2/XT | NVS 14-3/XT |
| --- | --- | --- |
| Image Intensifier Tube (IIT) | Image Intensifier Tube | 18 mm HyperGen | 18mm Gen 3 |
|  | Grade | XT |
|  | Photocathode operating diameter, mm | 18 |
|  | Photocathode type | S-25 | GaAs |
|  | Resolution, Lp/mm | 57-64 |
|  | Photocathode sensitivity, µA/lm | 600-750 | 1250 above |
|  | Luminous Gain, fL/fc, min. | 40,000 fl/fc at 10-6 fcd |
|  | Image magnification | 1 |
|  | Dark background brightness, max. cd/m² | 1,5x10-3 |
|  | Signal-to-noise ratio | 20-23 | 20-25 |
|  | Current consumption, max, mA | 15 |
|  | Mean time before failure, hours | 10,000 |
|  | Keep time, years | 15 |
| Magnification (standard) | 1x ( can add 4x or 5x lens directly, optional) |
| Field of view | 40° |
| Objective focal length, mm | 25 ~ ∞ |
| Objective F number | 1.2 |
| Eye relief, mm | 30 |
| Exit pupil diameter, mm | 25 |
| Focus range, m | 0.25 |
| Dioptric correction | ±5 |
| Power supply | Standard AA battery *1 or Standard CR123 battery *1 |
| Battery life, hours | 80 (I/R off) above 40 (I/R on) above |
| Low battery indicator | V |
| I/R ON indicator | V |
| Dimensions (include 1X lens), mm | Approx. 110x42x62 |
| Weight (include 1X lens), g | <320 |

- Adopt HyperGen or Gen 3 Image Intensifier Tube (IIT) with high FOM above 1250, which outperform the type of Gen. 3 in US export standard.

- With “Flip off” mask design, can “flip up” to shot off power quickly if using with helmet mount and rifle.

- Built-in 5mW infrared illuminator to enhance the illumination for using under complete darkness.

- Can work with DV camcorders & zoom lens.

- Compact, endurable construction, light weight, water immersion and easy to operate.

- Various optional C-mount objective lenses (4X, 10X or others) are interchangeable for long distance observation.

( Options:

- Binocular vision mount for combining two NVS-14

- 20x zoom lens, 10~200mm

- Helmet mount

- Quick release weapon mount

( Standard package:

- Main body of NVS-14

- Standard 25mm lens(1x), 30cm, 30 minutes immersed protection

- Head gear

- 25/30/37mm DV camcorder adapters

- Carry bag (with operation manual)

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.

Binocular vision