# Text boxes

Raysun DN-Super

D/N Long Distance Zoom Camera

Optics & Night Vision Devices - 27

* Suitable for 24h fire outbreak, security check,

rescue mission, coast line patrol,

riot control, disaster events monitoring.

* Optional wireless  transmission feature supports remote monitoring.

(Specification：

| Optical system |
| --- |
| Magnification | 20x |
| Focusing range | 10mm~200mm |
| Max aperture | F1.9 |
| Field of view | (Wide angle view) ≦33°x26°x19° (as a telescope) ≦1.5°x1.3°x1° |
| Lens diameter | 62mm |
| Image sensor | Sony Super HADCCDII |
| Digital image process | Double Scan DSP |
| Horizontal Resolution | 700TV Lines |
| Min lux | 0.001(IR off) |
| Auto shutter | 1/50 (1/60) ~1/100000 |
| Luminous gains(auto) | X2~X1024 |
| Recording system |
| Recording mode | General recording/Motion detection; with removable DVR for tactical use. |
| Support language | English、Japanese、Chinese |
| Operation | Manual/IR remote control |
| Time stamp | Y/M/D/H/M |
| Microphone | Live audio |
| Backlight time setting | OFF、30、60、180、300/sec |
| Video resolution | 720x480@30fps |
| Alert | Vibrating alert is given when on/off/low battery/full memory |
| Input system | NTSC/PAL |
| Output system | Real-time wireless transmission、USB、AV-out |
| Wireless transmission | Display on 2.5” monitor and do wireless transmission up to 50m |
| Power supply | Built-in rechargeable battery for continuous use of 8h. |
| Mount | 3 sets of 1913 rail to use with extra light source (with DC power source) |
| Weight | Around 3000g |
| Lighting system |
| Enhance illumination | Hand carry to monitor |
| Output power | CREE MC-E 10W LED(visible light) |
| Output luminosity | 900lumen (under strong mode) 4 light modes available: strong／medium／weak/flashing |
| Effective range | Up to 500m in night time |
| Light intensity | 1M: 13600Lux/20cm 2M: 3720Lux/40cm 3M: 1600Lux/70cm |
| Power | Built-in chargeable battery, |

Features

10W flashlight.

Hand-carry available

Able to use with 3W Laser IR Illuminator

High resolution A/V recording system + real-time wireless transmission by WIFI

Remote monitoring

on Tablet PC or mobile phone

Integrate 1913 rail with XY coordinate meter to adjust light projection angle in accordance with target position.

| Laser IR illuminator Specification |
| --- |
| IR spectrum | Above 880nm |
| IR output power | 1-3W adjustable |
| Projection angle | Adjustable 1~15 degree |
| Effective range | Recognize car ID no. up to 200m under complete darkness |
| Power supply | Built-in chargeable battery |

Option：

- Laser IR illuminator

(2). Tablet PC or

mobile phone

(3). High-grade tripod

(to reinforce stabilization.)

Standard package：

(1). D/N Long Distance cam

- TPL-10 LED illuminator

- See-Through filter

- Shoulder strap

- Carrying case

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.

3W Laser IR Illuminator

WiFi

- Adopt 20x zoom optical lens to enhance the  ability in recognition of car ID no. up to 200m and above if using with the IR laser illuminator under complete darkness.

Features：

| See through fog/mist | ＞ | See though rain | ＞ | Night vision | ＞ | Laser | ＞ |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Illumination | ＞ | Long distance observation | ＞ | Transmission | ＞ | Recording | ＞ |
| Photography | ＞ | Detection | ＞ |  |