-

# Text boxes

Multicopter Defender

RAYSUN MD-1S

Feature:

- Drone is now commonly used to spy personal privacy or top-secret information day and night, it’s also used as an invasive tool by using with weapon for illegal purpose, which has caused a serious problem on the sky, so Multicopter Defender is an ideal device to counter the threat nowadays.

- The shoulder rifle can block ISM and GPS signal to take down the drone immediately within 1,100m, when the drone is out of the owner’s range, it will either go home, make a controlled descent, or fall out of the sky, when the drone finds the way home, the user can catch the owner accordingly..

- Allow to disrupt the wireless video transmission which disables the on-site monitoring and guidance, the owner can’t wirelessly control the drone any more.

- With ability to use with night vision device or thermal scope for night time operation within 1100m.

- The high gain directional antenna can be free from environmental interference.

Specification:

Simulation:

1. Applicable GPS frequency: L1 / L2

2. Applicable ISM band()2.4G: 2400~2500 MHz

3. Applicable ISM band(5.8G): 5700~5900 MHz

4. Output power: Up to 30W and above.

5. Antenna gain: 10~12dBi, ERIP:up to 180dBm

6. Effective range: Above 1100M

Switch on GPS

GPS signal is missing, while flight condition can be tracked as well, which force the drone should be either controlled manually or descend slowly; auto-flight mode is not allowed.

Switch on GPS
GPS/Glonass/BeiDou is blocked

Switch on ISM
RC signal is blocked

Video:

Block GPS signal

Power on ISM.

The device is beyond owner’s control, while GPS function will guide the drone go back to the owner, so user can catch both targets easily.

10

Video: Take down the drone

Power on GPS and ISM

The drone completely

lose its control, and can be

only flying without any intention till drop to ground when running out of battery..

NVS-14 Night vision monocular

(option)

TS-75 Thermal scope (option)

Above 1100m

Effective range is up to 1100m

戰術滑軌結合強光照明

結合雷射瞄準

m

Roller carry case: easy to carry and store.

m

m

13~15dBi

Battery power indicator

with low power alert.

Vertical Beamwidth: 35(±3)°

1000m/300m

The built-in 1913 rail allows to attach various types of aimers or install a strap for shoulder-carry.

Horizontal Beamwidth: 40(±5)°

5

4

3

2

1

Antenna beamwidth

Option

1. Main unit

2. Roller carry case

3. Power cable

4. Charger

5. Handle-shape

support

Specification

Standard package

| Roller carry case size | 80 cm x 40.9 cm x 34.1 cm |
| --- | --- |
| Main unit size | 66 cm x 18.3 cm x 28 cm |
| Main unit size (including gunstock) | 86 cm x 18.3 cm x 28 cm |
| Weight | <6kg(including power system) |
| Operation voltage | DC 24V |
| Battery | 6400 m/Ah |
| Operation temperature | -10°~55° |
| Operation humidity | 95% |
| Protection standard | IP33 |
| Running time | 60 minutes |
| Charging time | Approx 4hours |
| Frequency | 1567~1583GHz 2400~2500GHz 5700~5900GHz |
| Output power | 20W(GPS、2.4G) 3W(5.8G) |
| Antenna output power | 12~15 dBi |
| Horizontal Beamwidth | 40(±5)degree |
| Vertical Beamwidth | 35(±3)degree |
| Effective range | Above 1100m |