# Text boxes

Multicopter Defender

RAYSUN MD-1

Feature:

- Drone is now commonly used to spy personal privacy or top-secret information day and night, it’s also used as an invasive tool by using with weapon for illegal purpose, which is caused a serious problem on the sky, so Multicopter Defender is an ideal device to counter the threat nowadays.

- The shoulder rifle can interfere with radio frequency of the drone within 3 seconds to trick it into believing it’s out of range of the owner, then the drone is programmed to either return to the owner, make a controlled descent, or fall out of the sky.The deviceallows to control ISM or GPS signal individually, for example, the user can only cut down ISM signal while keep GPS working to track the UAV owner's position and destroy it.

- With ability to use with night vision device or thermal scope for night time operation within 1100m.

- The high gain directional antenna can be free from environmental interference.

Specification:

Operation Instruction

Power on GPS

GPS signal is missing, while flight condition can be tracked as well, which force the drone should be either controlled manually or descend slowly; auto-flight mode is not allowed.

1. Applicable GPS frequency: L1 / L2

2. Applicable ISM band()2.4G: 2400~2500 MHz

3. Applicable ISM band(5.8G): 5700~5900 MHz

4. Output power: Up to 30W and above.

5. Antenna gain: 10~12dBi, ERIP:up to 180dBm

6. Effective range: Above 1100M

Switch on GPS
jammer GPS/Glonass/BeiDou is blocked

Video: Block GPS signal

Power on ISM.

The device is beyond owner’s control, while GPS function will guide the drone go back to the owner, so user can

catchboth targets easily.

10

Switch on ISM
jammer RC signal is blocked

Video: Take down the drone

24h Long Distance night vision system (option)

Power on GPS and ISM

The drone completely

loseits control, and can be

only flying without any intention.

The effective range is

up to 1100m

24h Thermal scope (option)

Above 1100M

戰術滑軌結合強光照明

結合雷射瞄準

UAV smuggling of firearms / drugs

UAV airdrop bomb

With battery capacity display and weak alarm function

UAV air photography infringement of privacy

UAV interference flight safety

Standard package

Specification

1. UAV Jammer main unit

2. Carrying case

3. external power cord

4. charger

5. tripod holder

6. hand-held bracket

| Length | 116 cm x 33 cm x 190 cm |
| --- | --- |
| Weight | Less than 6 Kg (Include battery、full set) |
| Voltage | DC 24V |
| Battery Capacity | 6400 m/Ah |
| Operational temperature | -10degree~55degree |
| Relative humidity | 95% |
| Protection Class | IP33 |
| Operation time | 60mins |
| Battery Charge time | 約4hours |
| Frequency range | 1560~1600GHz 2395~2490GHz 5710~5920GHz |
| Beam width (range) | ±15degree |
| Output Power | 20W(GPS、2.4G) 3W(5.8G) |
| Antenna output power | 12~15 dBi |
| Effective range | More than 1100 meter |

6

4

3

2

5

1

Optional Items

2.Thermal imager 
(With combination set)

1.Night vision device 
(With combination set)

The effective range is

up to 1100m