# Text boxes

3-shot Stun Gun

RAYSUN A-3

According to IEC 479-1 report, DC is 2-4 times safer than AC.

Powered by N2

gas.

AC

DC

Feature：

- 3-shot design: Allow to deploy 3 cartridges for multi-target defense up to 6m.

- Auto-rerloadl-system: The used cartridge can be auto ejected once release trigger; meantime, the next cartridge is auto refilled shortly, better than manual-control models in the market .

- Drive-stun capability: To stun the target by a direct contact with or without a cartridge installed.

- Two stunning modes: (1). Manual: Press to keep stunning as long as you want; the stunning function can be locked till handcuff the target. (2).Auto: To give 5-second electric shocks but pause 1-sec as a cycle and allow to repeat 3 cycles.

- Unique DC technology: To perform bigger power while much safer than traditional AC type;  according to IEC479-1 report, DC is 4 times safer than AC to human body.

- Reusable training cartridges: Designed for beginner to save your every penny.

- Integrated 1913 rails: Permit to attach external camera and illuminator for recording/illumination.

Specification：

Part name:

| Model | A-3 |
| --- | --- |
| Battery | Rechargeable lithium battery，7.4V, 1200mAh,DC, able to give continuous electric shock above 30 minutes. |
| Current | DC |
| Penetration | Around 2cm clothing |
| Peak open circuit arcing voltage | DC 30KV+10 |
| Frequency | 0Hz(DC) |
| Output current | <0.24mA(connect 100MΩimpedance load) |
| Temperature | -10°C ~ 55°C |
| Weight | <400g(excluding cartridges) |
| Dimension | 21.9 x 3.6 x 13.8cm |
| Warranty | One year |

Cartridge slot

(3 available)

Laser aimer

Manual/Auto
Power switch

Power

indicator

Contact stun button

Cartridge release button

Cartridge

availability indicator

Standard package：

Trigger

1

2

b

3

4

7

a

5

6

(1). A-3 Main unit

(2). 6m probe x 6

(3). Charger

(4). Holster

(5). Stretchable roller

(6). Belt clip

(7). Carry bag

Options：

(a) Training cartridge

(b) Tactical iIluminator

Safety button

Belt clip button

Charging jack