# Text boxes

Multi-functional

Airsoft Net Gun

Net Gun Catch Me

Features

- Entangle targets ability: Allow to capture a moving target without hurting them by firing a net to a distance of 8-10m.

- High shooting accuracy: Allowed to target directly to give a perfect shot and avoid the shooting failure problem on other types that needs to aim upward.

- Reused design: The net head can be reloaded and reused at a few minutes.

- Supplied training net: It’s Ideal for training purpose.

- Ultra slim net: With ability to reduce the wind blowback that is helpful to run further and faster.

- Easy carry: Provide quick-release belt clip to fasten on belt.

- No ammunition: No gun powder is used.

Specifications

Demonstration

| Material | Aluminum alloy |
| --- | --- |
| Weight for Aluminum weight | 13g |
| Weight quantity | 8 pieces |
| Effective range | up to 10 m |
| Optimum distance | 5-8 m |
| Net length(fully extend) | 3m x 3m |
| Mesh size | 15cm x 15cm |
| Intensity of pressure | 3.0Mpa |
| Power supply | 12g CO2 gas bottle(disposable) |
| Velocity | 10m/sec |
| Weight: | =<0.85Kg |
| Size | 75 x 48 x 250mm |

Training net

Catch Net

Standard package:

10

(1).Net gun main body

(2).Net head

(3).Training net

(4).12g CO2 gas bottle（NOT INCLUDE）

(5).CO2 gas bottle cartridge x2

(6). belt clip

(8).Carry bag

Quick release belt clip

shooting

Standby

Quick release

shooting

戰術滑軌結合強光照明

結合雷射瞄準