ZZZ

# Text boxes

RAYSUN Portable

4G AV Transmitter

GPS

Mobile

PC

DV camcorder

4G / LTE

Remote monitoring

Hidden camera

Analog CCD

Features

Tablet

- Compact and light weight, only palm size.

- Easy to operate, simply press one button to initiate the device.

- Integrate 4G/ LTE transmitter and GPS (option)，the H.265 codec enables to  compress data with minimized capacity while optimize the picture quality after decompress; the main unit supports FULLHD recording and send out HD video to remote site for monitoring.

- With ability to do multitask remote monitoring and recording via iOS、Android and PC，the user can download APP and scan QR to complete system installation.

- The supplied high resolution hidden camera and AV-input design permits to do either stationary or mobile surveillance.

- Support up to 128G SDXC , motion detection and circuit recording.

- Energy saving, allow to use with mobile power bank for long term recording.

Specification

Application

| RAYSUN 4G Transmitter |
| --- |
| Material | Aluminum alloy |
| Compressed | H.264/H.265 |
| Format | AVI/JPG |
| Recording | Standard/motion detection |
| Transmission | 4G LTE / 3G (micro SIM) |
| Antenna | Two antennas as interchange |
| GPS | Option |
| Time stamp | Auto |
| Memory | Support 128G SDXC MicroSD |
| Power supply | 5V / 1A |
| Frame rate | 10/15/20/25/30 fps(Adjustable) |
| Resolution | CIF/480P/720P/1080P |
| APP | Android/iOS |
| Weight | 81g |
| Size | 46.9x80.5x12.9mm |
| AV-in | Ø2.5/3.5mm AV input |
| LED indicator | Power /connection /recording |
| Digital camera |
| Sensor | 4 mega pixel CMOS |
| Aperture | F2.0 |
| Illuminating intensity | 0.1Lux |
| Field of view | 77.5° |

DV camcorder

Hidden camera

4G/LTE

Multitask monitoring

Standard package

10

1 .4G main unit x 1

2 .Antenna x 2

3 .Digital cam with accessories x 1

4 .Remote controller x 1

5 .Digital signal cable x 1

6 .Analog signal cable x 1

7 .Power cable x 1

8 Power supply x 1

9 . Analog signal

connecting cable x 1

8

5

1

2

7

6

3

4

9

戰術滑軌結合強光照明

結合雷射瞄準