(4)

# Text boxes

RAYSUN X-1 Plus

Multifunctional Stun Gun With Camcorder

Quickly mount to weapons for illuminating/aiming/recording.

Feature

- The best non-lethal devices with a detachable and robust carbon fiber body to meet demands on durability and maintenance.

- DC power is 2 ~ 4 times safer than AC power to human & animal body according to IEC TS 60479-1 from International Electro-technical Commission.

- Support 8 types of cartridges to immobilize the target or effectively intimidate/disperse the crowd or animals.

- With special design to resist high voltage, interference and vibration to ensure the recording quality. The device can automatically save the data every 3 minutes.

- Provide circulate recording to avoid missing any critical moment.

- Integrate LED light with 100m visible range.  (Remain all the X-1 functions)

- Adopt dual batteries to supply power for gun body and camcorder.

Standard pdackage

Specifications

| Name／Model | X-1 dedicated digital A/V Cam Recorder |
| --- | --- |
| Recording resolution | 1280x960／640x480 switchable |
| Lens | 0.6mm |
| Field of view | Around. 61 degree |
| Memory | Micro SD HC card |
| Date & Time display | YMD／HMS |
| File format | AVI |
| Record mode | Continuous |
| Frames per second | 24 fps／29 fps |
| Charging indication (green light) | Charging: ON／Full charged: OFF |
| Battery capacity | 550mA Li-on battery |
| Battery running time (exclude laser Pointer) | Around 80 minutes above |
| Low power indication | Red light flash |
| Data output port | USB 2.0 |
| Dimension | 66x59x37 mm |
| Weight | Around 52 g |
| LED light／Laser pointer | LED light: 3 switchable light modes: strong/weak/flashing. Laser red-dot pointer. -Wave length:: 645~665nm. -MTBF: 10,000 hours -Output power: Class IIIa–below 5mW |

(1) Raysun X-1 Plus Stun Gun Body (including camcorder + laser + LED light)

(2) 6m probe * 3

(3) Pepper powder cartridge *1

(4) Pepper bullet cartridge * 1

(5) Charger

(6) Safety plug-pin with wrist strap

(7) Belt/leg dual holster

(8) Carrying bag

(9) Operation manual, CD and target paper

Illustration

Record＋

Laser Pointer activated switch

(right side)

Record activated switch

(left side)

Laser Pointer

Low power indicator

(red light flash)

Recording resolution switch

Micro SD card slot

USB port

Protective cover

Reset switch

Powerful LED light